## Slide 1: Unit Testing of Flash Memory Device Driver through a SAT-based Model Checker
Moonzoo Kim and Yunho Kim
SWTV group, School of Computing, KAIST
Hotae Kim
Samsung Electronics, South Korea

## Slide 2: Summary of the Talk
In 2007, Samsung requested to debug the device driver for the OneNAND™ flash memory
We reviewed the requirement specifications, the design documents, and C code to identify code-level properties to check.
Then, we applied CBMC (C Bounded Model Checker) to check the properties
  Found several bugs
  Provided high confidence in multi-sector read operation through exhaustive exploration
OneNAND® Flash Memory Devices
Low Level
Device Driver
Block
Management
Sector
Translation
Demand
Paging
Manager
OS
Adapt-
ation
Module
Unified
Storage
Platform
Flash
Translation Layer
File
System
Notes: Two problems of model checking
Scalability
Separate model construction

## Slide 3: Overview
Background
  Logical-to-physical sector translation
  Overview of the Unified Storage Platform (USP)
  SAT-based model checking technique
Identification of properties to check
  High-level requirements
  Code-level properties
Unit analysis result through CBMC
  Prioritized read operation (PRO)@ Demand Paging Manager (DPM)
  Semaphore matching (SM)@ Block Management Layer (BML)
  Semaphore exception handling (SEH)@ STL~BML
  Multi-sector read operation (MSR) @ Sector Translation Layer (STL)
    NuSMV : BDD-based model checker
    Spin: Explicit model checker
    CBMC: C-bounded model checker
Lessons learned and conclusion

## Slide 4: Logical to Physical Sector Mapping
1:N mapping from a LUN to PUNs
Sector mapping
Sector Allocation Map (SAM)
In flash memory, logical data are distributed over physical sectors.
Notes: Each logical unit is mapped to a linked list of physical units because one logical sector may consume several physical sectors through updates. So there is 1:N mapping from a logical unit to physical units. A simple sector mapping example is as follows. First logical unit has an empty physical unit. A new logical sector, LS0, is written in the physical sector0. Similarly LS1 is written in LS1. Then when LS1 is updated, PS1 is invalidated and LS1 is written in PS2 and so on. Sector allocation map keeps the Logical sector to physical sector mapping. SAM have information what physical sector stores a given logical sectors. for example when we read logical sector 0, then we find the physical sector offset from the logical sector offset 0 from SAM. If the physical offset is empty, then read operation traverse a linked list until find a physical offset or traverse all physical sector in a linked list.

## Slide 5: Overview of the OneNAND® Flash Memory
OneNAND® Flash Memory Devices
Low Level (LLD)
Device Driver
Block
Management (BML)
Sector
Translation (STL)
Demand
Paging
Manager (DPM)
OS
Adapt-
ation
Module
Unified
Storage
Platform
App1
App2
App3
Source:
Software Center
of Samsung
Electronics ‘06
Characteristics of OneNAND® flash
  Each memory cell can be written limited number of times only
    Logical-to-physical sector mapping
    Bad block management
    Wear-leveling
  XIP by emulating NOR interface through demand-paging scheme
    Multiple processes access the device concurrently
    Urgent read operation should have a higher priority
    Synchronization among processes is crucial
  Performance enhancement
    Multi-sector read/write
    Asynchronous operations
    Deferred operation result check
Flash
Translation Layer
File
System
Moonzoo Kim et al. Provable SW Lab
Unit Testing of Flash Memory Device Driver through a SAT-based Model Checker
5/27
PRO
SM
SEH
MSR
‘08 Spin Workshop

## Slide 6: C Bounded Model Checker (CBMC)
Handles function calls using inlining
Unwinds the loops a fixed number of times (bounded MC)
  A user has to know a upper bound of each loop
    Loops often have clear upper bounds
    We can still get debugging result without upper bounds
Specifies constraints to describe an environment of the target program, which can model non-deterministic user inputs, or multiple scenarios
  Ex. __CPROVER assume(0<=nDev && nDev<=7)
  Ex.__CPROVER_assume( SHDC.nPhySctsPerUnit == SHPC.nBlksPerUnit * SHVC.nPgsPerBlk * SHVC.nSctsPerPg)
Checks properties by assertions
Moonzoo Kim et al. Provable SW Lab
Unit Testing of Flash Memory Device Driver through a SAT-based Model Checker
6/27

## Slide 7: Project Overview
The goal of the project
  To check whether USP conforms to the given high-level requirements
    we needed to identify the code-level properties to check from the given high-level requirements
A top-down approach to identify the code level properties from high-level requirements
  USP has a set of elaborated design documents
    Software requirement specification (SRS)
    Architecture design specification (ADS)
    Detailed design specification (DDS)
      DPM, STL, BML, and LLD

## Slide 8: Three High-level Requirements in SRS
SRS specifies 13 functional requirements, 3 of which have “very high” priorities
  Support prioritized read operation
    To minimize the fault latency, USP should serve a read request from DPM prior to generic requests from a file system.
    This prioritized read request can preempt a generic I/O operation and the preempted operation can be resumed later.
  Concurrency handling
    BML and LLD should avoid a race condition or deadlock through synchronization mechanisms such as semaphores and locks.
  Manage sectors
    STL provides logical-to-physical mapping, i.e. multiple logical sectors written over the distributed physical sectors should be read back correctly.

## Slide 9: Top-down Approach to Identify Code-level Property
Concurrency handling
Prioritized
read
Multi-sector
read
Page fault handling while a device is being programmed
Check “Step 18. store the status”
Check “Step 14. wait until the device is ready ”
Page fault handling while a device is being read
SRS
ADS
DDS
C
Code
Is the status really stored?
At line 494 of PriRead() in LLD.c
assert(bNeedToSave->saved)
Legend
Spec. in the
design docs
User defined
property to check
MMU
Page Fault
Handler
Page Cache
Management
BML
LLD
: OneNAND
Device
If there is a free frame,
go to Step6.
1: issue page fault exception
7: find a location where the page is stored in OneNAND device
8: request read operation
9: request read operation
13: check if the device is ready
15: check the NeedToSave flag
16: request the operation status
17: return the operation status
18: store the status
11: request the ready/busy status
12: return the ready/busy status
10: Set the Preempted flag
2: request a free frame in page cache
3: find a free frame
4: find a victim page
5: page out the victim page
6: return the free fram
In case of busy status
because of program
operation
14: wait until the device is ready
A sequence diagram of page fault handling
while a device is being programmed in LLD DDS
Total 43 code-level properties are identified

## Slide 10: Results of Unit Testings
Prioritized read operation
  Detected a bug of not saving the status of suspended erase operation
Concurrency handling
  Confirmed that the BML semaphore was used correctly
  Detected a bug of ignoring BML semaphore exceptions
Multi-sector read operation (MSR)
  Provided high assurance on the correctness of MSR, since no violation was detected even after exhaustive analysis (at least with a small number of physical units(~10))
Notes: Note that bounds for most loops in USP can be obtained easily based on the physical characteristics of OneNAND device
    E.g. # of sectors per a unit,

## Slide 11: A Bug in PriRead()
We added a flag saved to denote whether the status of the preempted operation is saved
CBMC detected the given assertion was violated when an erase operation was preempted
  It takes 8 seconds and 325 Mb on the 3Ghz Xeon machine
  CBMC 2.6 with MiniSAT 1.1.4
01:...
02:State 14 file LLD.c line 408 function PriRead thread 0
03: LLD::PriRead::1::bEraseCmd=1
04:State 15 file LLD.c line 412 function PriRead thread 0
05: LLD::PriRead::1::1::2::nWaitingTimeOut=…
06:State 17 file LLD.c line 412 function PriRead thread 0
07: LLD::PriRead::1::1::2::nWaitingTimeOut=…
08:...
09:Violated property:
10: file LLD.c line 424 function PriRead
11: assertion !(_Bool)pstInfo->bNeedToSave || (_Bool)saved
12:VERIFICATION FAILED
374: VOID PriRead(Read(UINT32 nDev, UINT32 nPbn, UINT32 nPgOffset) {
…
416: if ((bEraseCmd==FALSE32) && (pstInfo->bNeedToSave==TRUE32)) {
417: pstInfo->nSavedStatus = GET_ONLD_CTRL_STAT(pstReg, ALL_STATE);
418: pstInfo->bNeedToSave = FALSE32;
419: saved=1; // added for verification purpose }
…
424: assert(!(pstInfo->bNeedToSave) || saved);

## Slide 12: BML Semaphore Usage
The standard requirements for a binary semaphore
  Semaphore acquire should be followed by a semaphore release
  Every function should return with a semaphore released
    unless the semaphore operation creates an exception error.
There exist 14 BML functions that use the BML semaphore.
  We inserted an smp to indicate the status of the semaphore
  and simple codes to decrease/increase smp at the corresponding semaphore operation.
CBMC concluded that all 14 BML functions satisfied the above two properties.
  Consumes 10 seconds and 300 megabytes of memory on average to analyze each BML function

## Slide 13: BML Semaphore Exception Handling (1/2)
The BML semaphore operation might cause an exception depending on the hardware status.
Once such BML semaphore exception occurs, that exception should be propagated to the topmost STL functions to reset the file system
  We checked this property by the following assert statement inserted before the return statement of the topmost STL functions:
  assert(!(SMerr==1)||nErr==STL CRITICAL ERR)
Bug detected
Topmost STL functions

## Slide 14: BML Semaphore Exception Handling (2/2)
CBMC analyzed a call graph of each of the topmost STL functions and detected that BML semaphore exception might not propagate due to bug at _GetSInfo()
The bug was detected when loop bound was set 2 with ignoring loop unwinding assertion.
  Memory overflow occurred with the loop bound 3
For STL_Write(), this verification task consumed 616 megabytes of memory in 97 seconds
  Each call sequence is around 1000 lines long on average.
Bug detected
Topmost STL functions

## Slide 15: Multi-sector Read Operation (MSR)
MSR reads adjacent multiple physical sectors once in order to improve read speed
  MSR is 157 lines long, but highly complex due to its 4 level loops
We built a small test environment for MSR
  The test environment contains only upto 10 physical units
  The test environment should follow constraints, which are described by _CPROVER_assume(Boolean exp) statement
    SAM tables and PUs should correspond each other
    For each logical sector, at least one physical sector that has the same value exists
1 |  |  | 0 | 
 | 1 |  |  | 1
 | 2 |  |  | 
 |  | 3 |  | 
 |  |  | E | 
A | B |  |  | F
 | C |  |  | 
 |  | D |  | 
 | 3 |  |  | 3
0 |  |  | 2 | 
3 |  |  |  | 
 | 1 |  |  | 
Sector 0
Sector 1
Sector 2
Sector 3
PU0~PU4
A distribution of “ABCDEF”
B |  |  |  | 
 | D |  |  | 
 |  |  | F | 
C | A |  |  | E
PU0~PU4
SAM0~SAM4
SAM0~SAM4
b) Another distribution of “ABCDEF”
LU0
LU1
LU0
LU1
LU0
LU1
LU0
LU1
Assumptions:
- 1 Unit = 4 sectors=4 Bytes
- LU0: [LS0(‘A’),LS1(‘B’),LS2(‘C’),LS3(‘D’)]
- LU1: [LS4(‘E’),LS5(‘F’)]
a) LU0 is mapped to [PU0,PU1,PU2]
LU1 is mapped to [PU3,PU4]
b) LU0 is mapped to [PU2,PU1]
LU1 is mapped to [PU3,PU4]

## Slide 16: Loop Structure of MSR
01:curLU = LU0;
02:while(numScts > 0 ) {
03: readScts = # of sectors to read in the current LU
04: while(readScts > 0 ) {
05: curPU = LU->firstPU;
06: while(curPU != NULL ) {
07: while(...) {
08: conScts = # of consecutive PS’s to read in curPU
09: offset = the starting offset of these consecutive PS’s in curPU
10: }
11: BML_READ(curPU, offset, conScts);
12: readScts = readScts - conScts;
13: curPU = curPU->next;
14: }
15: }
16: curLU = curLU->next;
17:}
Loop1: iterates over LUs until all data are read
Loop2: iterates until the current LU is read completely
Loop3: iterates over PUs linked to the current LU
Loop4: identify consecutive PS’s in the current PU
MSR reads consecutive physical sectors together for improving read performance
Statistics
  157 lines long, 4 level nested loops
  4 parameters to specify logical data to read (from where, to where, how long, read flag

## Slide 17: Environment Model
Environment model creation
  The environment of MSR (i.e., PUs and SAMs configurations) can be described by invariant rules. Some of them are
    One PU is mapped to at most one LU
    Valid correspondence between SAMs and PUs:
    If the i th LS is written in the k th sector of the j th PU, then the i th offset of the j th SAM is valid and indicates the k’th PS ,
    Ex> 3rd LS (‘C’) is in the 3rd sector of the 2nd PU, then SAM1[2] ==2
    i=2 k=2 j=1
    3. For one LS, there exists only one PS that contains the value of the LS:
    The PS number of the i th LS must be written in only one of the (i mod 4) th offsets of the SAM tables for the PUs mapped to the corresponding LU.
1 |  |  | 0 | 
 | 1 |  |  | 1
 | 2 |  |  | 
 |  | 3 |  | 
 |  |  | E | 
A | B |  |  | F
 | C |  |  | 
 |  | D |  | 
Sector 0
Sector 1
Sector 2
Sector 3
PU0~PU4
SAM0~SAM4
Notes: NuSMV is a symbolic model checker. Symbolic model checker represents a system model with a compact boolean formula. Because It does not store explicit state spaces, it is believed that symbolic model checker can handle large state space That is the reason why we use NuSMV first.
The modeling language of NuSMV is quite different from C. Therefore NuSMV model is quite long and hard to make. In our project, the most difficult and time consuming job is to make a NuSMV model. Moreover the verification performance is much worse than we expected.

## Slide 18: Exponential Increase of Distribution Cases
Chart: Possible cases
| 5 | 10 | 15 | 20
5 | 290304 | 26297568 | 329505792 | 1935398976
6 | 1416960 | 270341280 | 5238466560 | 41737406400
7 | 7338240 | 3439782720 | 106013629440 | 1157911862400
8 | 42013440 | 50443272000 | 2497181230080 | 37567743166080
n: # of physical units
l: # of logical sectors (<=8)
1 unit consists of 4 sectors

## Slide 19: MSR Model Checking Results
Verification of MSR by using NuSMV, Spin, and CBMC
  NuSMV: BDD-based symbolic model checker
  Spin: Explicit model checker
  CBMC: C-bounded model checker
The requirement property is to check
  after_MSR -> (∀i. logical_sectors[i] == buf[i])
We compared these three model checkers empirically

## Slide 20: Excerpts of the SMV Model
MODULE main
-- Variable declaration
VAR
SAM : array 0..4 of sam_type;
PU : array 0..4 of PU_type;
buf : array 0..4 of 0..5;
nScts : 0..5;
-- SPEC
INVARSPEC (after_first_do ->
PU[0].sect[0]=1 &
PU[0].sect[1]=2 &
PU[0].sect[2]=3 &
PU[0].sect[3]=4 &
PU[3].sect[0]=5)
init(buf[0]):=0;
-- if( pBuf==0 && 0 < nScts )
-- buf[0]= PU[PU_id].sect[nFirstOffset]
next(buf[0]):
case after_fourth_do :
case pBuf = 0 & 0 < nScts: -- i=0
case
PU_id=0 & nFirstOffset=0: PU[0].sect[0];
PU_id=0 & nFirstOffset=1: PU[0].sect[1];
PU_id=0 & nFirstOffset=2: PU[0].sect[2];
PU_id=0 & nFirstOffset=3: PU[0].sect[3];
…
PU_id=4 & nFirstOffset=3 : PU[4].sect[3];
esac;
esac;
init(buf[1]):=0;
next(buf[1]):= …

## Slide 21: Verification Performance of NuSMV
Verification was performed on the machine equipped with Xeon5160 (3Ghz, 32Gbyte Memory), 64 bit Fedora Linux 7, NuSMV 2.4.3
The requirement property was proved correct for all the experiments (i.e., MSR is correct in this small model)
    For 7 sectors long data that are distributed over 7 PUs consumes more than 11 hours while consuming only 550 mb memory

## Slide 22: Excerpts of the Spin Model
active proctype SM_ReadSectors() {
byte buf[NUM_LS_USED];
byte nScts;
byte nFirstOffset;
byte nNumOfScts=NUM_LS_USED;
byte nReadScts=nNumOfScts;
byte nSamIdx;
do /* 1047: while (nNumOfScts >0) { */
:: nNumOfScts > 0 ->
PU_id = lui[nLun];
if /* nReadScts = ... */
:: (SECT_PER_U-nSamIdx)> nNumOfScts ->
nReadScts = nNumOfScts;
:: else->nReadScts =SECT_PER_U- nSamIdx;
fi;
nNumOfScts = nNumOfScts - nReadScts;
do /* line 1068: while (nReadScts > 0) */
:: (nReadScts > 0) -> PU_id = lui[nLun];
nFirstOffset=255;
nScts=1; nReadScts--;
do /* line 1075: do {... */
:: true;
if /* line 1077: if(pstCurrent->pSam[nSamIdx]...*/
:: SAM[PU_id].valid[nSamIdx]-> nFirstOffset = SAM[PU_id].offset[nSamIdx];nSamIdx++;
do /* line 1084:while (nReadScts > 0) { ...} */
:: (nReadScts > 0) ->
if
::FirstOffset+nScts==
SAM[PU_id].offset[nSamIdx] ->
nScts++;nReadScts--;nSamIdx++;
:: else-> break;
fi;
:: else->break;
od;
BML_MRead(PU_id,nFirstOffset,nScts,pBuf);
break;
:: else;
fi;
if /*line 1112: } while ( PU[PU_id].nil != true) */
:: PU[PU_id].nil -> break;
:: else;
fi;
PU_id++;
od;
}

## Slide 23: Verification Performance of Spin
The requirement property was satisfied
The data abstraction technique shows significant performance improvement upto 78% of memory reduction and 35% time reduction (for 5 logical sectors data)
Chart: A number of physical units
| 5 | 6 | 7 | 8 | 9 | 10
5(abs) | 2.14 | 7.295 | 20.307 | 49.233 | 110.315 | 230.006
6(abs) | 10.894 | 46.332 | 158.358 | 455.847 | 1193.245 | 3004.627
7(abs) | 62.465 | 361.249 | 1604.86
8(abs) | 403.123 | 3475.25
5 | 2.773 | 9.61 | 27.585 | 71.873 | 168.009 | 355.587
6 | 14.07 | 62.824 | 241.067 | 853.667
7 | 83.818 | 602.704
8 | 684.822
Chart: A number of physical units
| 5 | 6 | 7 | 8 | 9 | 10
5(abs) | 290.01 | 339.981 | 463.373 | 728.384 | 1242.023 | 2162.804
6(abs) | 371.111 | 688.346 | 1625.818 | 3975.488 | 9190.925 | 19736.692
7(abs) | 797.504 | 3074.471 | 11398.26
8(abs) | 3966.682 | 26098.394
5 | 348.071 | 552.666 | 1089.959 | 2310.26 | 4851.52 | 9672.7
6 | 654.656 | 1946.023 | 6083.597 | 17093.031
7 | 2324.084 | 12050.752
8 | 12303.68
(a) Time consumption
(b) Memory consumption

## Slide 24: Modeling by CBMC
CBMC does not require an explicit target model creation
An environment for MSR was specified using assume statements and the environment model was similar to the environment model in NuSMV
For the loop bounds, we can get valid upper bounds from the loop structure and the environment setting
  The outermost loop: L times (L is a # of LUs)
  The 2nd outermost loop: 4 times (one LU contains 4 LS’s)
  The 3rd outermost loop: M times
  (M is a # of PUs)
  The innermost loop: 4 times
  (one PU contains 4 PS’s)
1 |  |  | 0 | 
 | 1 |  |  | 1
 | 2 |  |  | 
 |  | 3 |  | 
 |  |  | E | 
A | B |  |  | F
 | C |  |  | 
 |  | D |  | 
Sector 0
Sector 1
Sector 2
Sector 3
PU0~PU4
SAM0~SAM4
L=2, M=5

## Slide 25: Verification Performance of CBMC
Exponential increase in both time and memory. However, the slope is much lower than those of NuSMV and Spin, which makes CBMC perform better for large problems
A problem of 10 PUs and 8 LS’s has 8.6x105 variables and 2.9 x 106 clauses.
Chart: A number of physical units
| 5 | 6 | 7 | 8 | 9 | 10
5 | 15.867 | 28.111 | 44.019 | 76.828 | 119.359 | 149.468
6 | 40.221 | 59.278 | 113.122 | 188.771 | 290.608 | 380.755
7 | 63.571 | 111.149 | 203.023 | 348.882 | 706.514 | 895.606
8 | 102.683 | 280.506 | 458.238 | 809.804 | 1372.795 | 2059.568
Chart: A number of physical units
| 5 | 6 | 7 | 8 | 9 | 10
5 | 48.92 | 62.77 | 69.48 | 82.21 | 96.55 | 110.96
6 | 88.8 | 103.02 | 128.15 | 142.07 | 197.02 | 224.09
7 | 93.84 | 108.76 | 148.2 | 172.83 | 243.42 | 314.56
8 | 108.55 | 147.49 | 189.42 | 256.63 | 389.7 | 342.54
(a) Time consumption
(b) Memory consumption
Notes:   1.7x105 conflicts, 106 decisions, and 4.8x109 propagations

## Slide 26: Performance Comparison
Chart: Time complexity LS = 6
| 5 | 6 | 7 | 8 | 9 | 10
Spin | 10.894 | 46.332 | 158.358 | 455.847 | 1193.245 | 3004.627
NuSMV | 421 | 418 | 11832 | 13210
CBMC | 40.221 | 59.278 | 113.122 | 188.771 | 290.608 | 380.755
Chart: Space complexity LS = 6
| 5 | 6 | 7 | 8 | 9 | 10
Spin | 371.111 | 688.346 | 1625.818 | 3975.488 | 9190.925 | 19736.692
NuSMV | 72 | 82 | 371 | 405
CBMC | 88.8 | 103.02 | 128.15 | 142.07 | 197.02 | 224.09

## Slide 27: Conclusion
We successfully applied CBMC to detect hidden bugs in the device driver for Samsung’s OneNAND flash memory
  Also, we established confidence in the correctness of the complex MSR
Lessons learned
  Software model checker as an effective unit testing tool
    CBMC took modest amount of memory and time to detect bugs in USP
    Exhaustive analysis can detect hidden bugs
  Advantages of a SAT-based model checker
    Analysis capability of whole ANSI-C
    No abstract model required
We believe that a SAT-based model checker can be utilized effectively as a unit testing tool to complement conventional testing